## Slide 1: Tutorial No. 11
Module 10

## Slide 2: Q1
The OS of an 80286 processor supports non-preemptive priority scheduling.
There are 5 threads that have to be scheduled.
The tasks and priority are shown in the table below.
Give the order of the threads scheduled in the 1st five timeslots.
Thread | TH1 | TH4 | TH2 | TH5 | TH3
Priority | 1 | 2 | 3 | 4 | 5

## Slide 3: Q2
The following data is present in memory of size 16 locations
0000 | F8
0001 | 56
0010 | 3A
0011 | 79
0100 | 67
0101 | 8D
0110 | 9B
0111 | 78
1000 | 91
1001 | AD
1010 | BC
1011 | 78
1100 | 96
1101 | 70
1110 | 00
1111 | FF

## Slide 4
If the data is read by the processor in the following order from the addresses
0000
0001
0100
1000
Show the contents of the cache for direct-mapped; four line cache with each read operation.

## Slide 5: Solution
Main Memory Address – 4 bits
Cache – 4 line
Address – 2 bits
Block No. – 2bits Tag 2- bits
00 01

## Slide 6: Solution
Block | Tag | Data
00 |  | 
01 |  | 
10 |  | 
11 |  | 

## Slide 7: Solution – After 1st read
Block | Tag | Data
00 | 00 | F8
01 |  | 
10 |  | 
11 |  | 
Cold Miss

## Slide 8: Solution – After 2nd read
Block | Tag | Data
00 | 00 | F8
01 | 00 | 56
10 |  | 
11 |  | 
Cold Miss

## Slide 9: Solution – After 3rd read
Block | Tag | Data
00 | 00 | F8
01 | 00 | 56
10 |  | 
11 |  | 
Conflict Miss

## Slide 10: Solution – After 3rd read
Block | Tag | Data
00 | 01 | 67
01 | 00 | 56
10 |  | 
11 |  | 
Conflict Miss

## Slide 11: Solution – After 4th read
Block | Tag | Data
00 | 01 | 67
01 | 00 | 56
10 |  | 
11 |  | 
Conflict Miss

## Slide 12: Solution – After 4th read
Block | Tag | Data
00 | 10 | 91
01 | 00 | 56
10 |  | 
11 |  | 
Conflict Miss

## Slide 13: Q3
Repeat the problem if the cache for 2 way set associative, two line cache after every read operation.

## Slide 14: Solution
Main Memory Address – 4 bits
Cache – 4 line
Address – 1 bit
Block No. – 1 bit Tag 3- bits
0001

## Slide 15: Solution
Block | Tag | Data | Tag | Data
0 |  |  |  | 
1 |  |  |  | 
 | Set 0 |  | Set 1 | 

## Slide 16: Solution – After 1st read
Block | Tag | Data | Tag | Data
0 | 000 | F8 |  | 
1 |  |  |  | 
 | Set 0 |  | Set 1 | 
Cold Miss

## Slide 17: Solution – After 1st read
Block | Tag | Data | Tag | Data
0 | 000 | F8 |  | 
1 |  |  |  | 
 | Set 0 |  | Set 1 | 
Cold Miss

## Slide 18: Solution – After 2nd read
Block | Tag | Data | Tag | Data
0 | 000 | F8 |  | 
1 | 000 | 56 |  | 
 | Set 0 |  | Set 1 | 
Cold Miss

## Slide 19: Solution – After 3rd read
Block | Tag | Data | Tag | Data
0 | 000 | F8 | 010 | 67
1 | 000 | 56 |  | 
 | Set 0 |  | Set 1 | 
Cold Miss

## Slide 20: Solution – After 4th read
Block | Tag | Data | Tag | Data
0 | 000 | F8 | 010 | 67
1 | 000 | 56 |  | 
 | Set 0 |  | Set 1 | 
Conflict Miss

## Slide 21: Solution – After 4th read
Block | Tag | Data | Tag | Data
0 | 100 | 91 | 010 | 67
1 | 000 | 56 |  | 
 | Set 0 |  | Set 1 | 
Conflict Miss

## Slide 22: Q 4
Assume that the system has a two-level cache:
The level-1 cache has a hit rate of 90% and the level-2 cache has a hit rate of 97%.
The level 1 cache access time is 4 ns, the level 2 cache access time is 15ns and access time of main memory is 80 ns.
What is the average memory access time?

## Slide 23: Solution
h1 – 0.9
h2 - 0.1 x 0.97
tav = h1tL1 + h2tL2 + (1-h1 -h2)tmain
tav = 0.9 x 4ns + 0.097 x 15ns + (1-0.9-0.097) 80ns
5.295 ns

## Slide 24: Q5
Processor - 80286
GDTR – 100000H

## Slide 25
GDT
Address | Data |  |  |  |  |  |  | 
100008 | 00 | 00 | 82 | 01 | 00 | 00 | FF | FF
100010 | 00 | 00 | 93 | 20 | 00 | 00 | 00 | 7F
100018 | 00 | 00 | 83 | 03 | 00 | 00 | 00 | 3F
100020 | 00 | 00 | A1 | 0A | 00 | 00 | 00 | 1F
100028 | 00 | 00 | DF | B0 | 00 | 00 | 01 | FF
100030 | 00 | 00 | 92 | B1 | 00 | 00 | 0F | FF
100038 | 00 | 00 | BF | 7B | 00 | 00 | 3F | FF
100040 | 00 | 00 | D2 | 7A | 00 | 00 | 07 | FF
100048 | 00 | 00 | 9F | A1 | 00 | 00 | 1F | FF
100050 | 00 | 00 | C4 | 02 | 00 | 38 | 10 | 00
100058 | 00 | 00 | 85 | 00 | 00 | 20 | 00 | 00
100060 | 00 | 00 | B3 | 50 | 00 | 00 | 1F | FF

## Slide 26
LDT 1
Address | Data |  |  |  |  |  |  | 
010000 | 00 | 00 | 82 | 01 | 00 | 00 | FF | FF
010008 | 00 | 00 | 82 | 20 | 00 | 00 | FF | FF
010010 | 00 | 00 | 83 | 03 | 00 | 00 | 00 | 3F
010018 | 00 | 00 | FC | 0A | 00 | 00 | 00 | 1F
010020 | 00 | 00 | DF | B0 | 00 | 00 | 01 | FF
010028 | 00 | 00 | 92 | B1 | 00 | 00 | 0F | FF
010030 | 00 | 00 | B2 | 7B | 00 | 00 | 03 | FF
010038 | 00 | 00 | D2 | 7A | 00 | 00 | 07 | FF
010040 | 00 | 00 | 9F | A1 | 00 | 00 | 1F | FF
010048 | 00 | 00 | B3 | A3 | 00 | 00 | 3F | FF
010050 | 00 | 00 | B3 | B1 | 00 | 00 | FF | FF
010058 | 00 | 00 | 82 | 50 | 00 | 00 | 1F | FF

## Slide 27
LDT 2
Address | Data |  |  |  |  |  |  | 
200000 | 00 | 00 | 82 | 01 | 00 | 00 | FF | FF
200008 | 00 | 00 | 82 | 20 | 00 | 00 | FF | FF
200010 | 00 | 00 | 83 | 03 | 00 | 00 | 00 | 3F
200018 | 00 | 00 | FC | 0A | 00 | 00 | 00 | 1F
200020 | 00 | 00 | DF | B0 | 00 | 00 | 01 | FF
200028 | 00 | 00 | 92 | B1 | 00 | 00 | 0F | FF
200030 | 00 | 00 | B2 | 7B | 00 | 00 | 03 | FF
200038 | 00 | 00 | D2 | 7A | 00 | 00 | 07 | FF
200040 | 00 | 00 | 9F | A1 | 00 | 00 | 1F | FF
200048 | 00 | 00 | B3 | A3 | 00 | 00 | 3F | FF
200050 | 00 | 00 | 82 | B1 | 00 | 00 | FF | FF
200058 | 00 | 00 | B3 | 50 | 00 | 00 | 1F | FF

## Slide 28
Current CPL – 10
CALL 0051H , [1200H]

## Slide 29: Solution
7B 10 00H

## Slide 30
Current CPL 00
CALL 0058H , [1400H]

## Slide 31
0000 0000 0000 0000 | Link | 
ESP0 |  | 
0000 0000 0000 0000 | SS0 | 
ESP1 |  | 
0000 0000 0000 0000 | SS1 | 
ESP2 |  | 
0000 0000 0000 0000 | SS2 | 
CR3 |  | 
EIP | (00 00 10 00) | 
EFLAGS |  | 
EAX |  | 
ECX |  | 
EDX |  | 
EBX |  | 
ESP |  | 
EBP |  | 

## Slide 32
ESI |  | 
EDI |  | 
0000 0000 0000 0000 | ES | 
0000 0000 0000 0000 | CS (5000) | 
0000 0000 0000 0000 | SS | 
0000 0000 0000 0000 | DS | 
0000 0000 0000 0000 | FS | 
0000 0000 0000 0000 | GS | 
0000 0000 0000 0000 | LDT | 
Available |  | T
Available to user |  |