## Slide 1: Microprocessor Programming & Interfacing
Tutorial 3
Module 4

## Slide 2: Q1.
Write an ALP that will copy a set of 10 bytes from memory location loc1 to memory location loc2 in the reverse order.

## Slide 3: Q2.
An array of data is stored in data segment starting at ARRAY1.
The number of elements in the array is stored in location COUNT1.
Write a program to count the number of occurrences of the element in CODE1 in the ARRAY1 and store this result in location RESULT1.

## Slide 4: Q3.
An interleaved string is stored from displacement ‘istr1’.
The size of the interleaved string is stored in location ‘cnt1’.
Write an ALP that will separate the interleaved string into two strings
If the interleaved string is “hmeilclroo” it should be separated as two strings “hello” and “micro”.
You can assume that the strings to be separated will be of equal size. [note – there is no need to use string instructions for this]

## Slide 5: Q4. For an 8086 Processor
.Model Tiny
. DATA
DAT1 DB 45H, 54H, 46H
ALIGN 2
P1 EQU 97H
DAT2 DW 23F8H, 2435H
DAT3 DB ’INTER’
DAT4 DB 6 DUP (122)
DAT5 DB 3 DUP (?)
DAT6 DW 33H
DAT7 DB 0FH
.CODE
.STARTUP
.EXIT
END
DS:0118H |  |  |  |  |  |  |  | 
DS:0120H |  |  |  |  |  |  |  | 
DS:0128H |  |  |  |  |  |  |  | 
Write the contents of memory in data segment that result from data declarations
You may use ‘A’ to represent ASCII byte for the character A.
If the contents cannot be determined put a ‘X’ in the box.
All values except for ASCII values must be in hexadecimal

## Slide 6: Q6.
An array of data is stored in data segment starting from ARRAY1.
The number of elements in the array is stored in location COUNT1.
Size of data is 16-bit
Write an ALP to find the minimum number and the displacement at which it is stored.
The number must be stored in memory location MIN and the address of the number in memory location MINADDR.