## Slide 1: Tutorial 7
Module 5

## Slide 2: Question 1
What are the signals available on the system bus?
Can ALE inverted be used instead of DEN for enabling the transceivers?
What signals of 8088 are different from 8086 ?
Notes: A0- A19, D0-D15 IOR IOW MEMR MEMW
No as DEN should go low only after RD/WR signal
Data and M/IO

## Slide 3: Question 2 -Give the machine cycles that have to be carried out for the following instructions for 8086
Call AX
RET (near)
ADC AX,BX
ADD AX,[BX]
DEC WORD PTR [SI]
MOV CX,DX
ADD [BX+SI+1000H] , CX
CMP [SI],AX
XCHG AX,[BX]
NOP
ROL BYTE PTR [2000], CX (CX has a count of 7)
Notes: 1 MEMR, I MEMW,
1 MEMR, I MEMR
1 MEMR
1 MEMR, 1 MEMR
1 MEMR, 1 MEMR, 1 mEMW
1 MEMR
1 MEMR, 1 MEMR, 1MEMR, 1 MEMW
1 MEMR, 1 MEMR

## Slide 4
T1
T2
T3
T4
A19 – A16
S7 – S3
A15-A0
Data
A19-A16/S6–S3
CLK
AD19- AD16
M/IO’
ALE
DT/R’
RD’
DEN’
200 ns
800 ns
Address Setup
Data Setup
Bus Timings for a Read Operation
Tw
Notes: Typically address setup for 5 MHz is 50 – 60 % of clock
Data set up < 20 % of clock
Delay by buffers add 20 %

## Slide 5: Question 3
If an 8086 processor is working at 5 MHz – how much time does 1 MEMR cycle take
  If there no wait states
  If there is 1 wait state
If a processor is working at 5 MHz and the memory access time is 750ns. The number of wait states required will be , considering an address set-up time of 110ns, data set-up time of 40ns with a latching and buffer delays of 30ns.
Notes: MEMR – 0.2 x 4s = 0.8
MEMR with wait 0.2 x 5
1 wait state