## Slide 1: Tutorial - 10
Module 8

## Slide 2: Q1
An 8086 system is used for controlling the speed of a motor. The motor can operate at 5 different speeds (1-5).
The speed is changed by changing the duty cycle of a PWM input of frequency 100 Hz to the motor’s driver circuit.
The PWM duty cycle changes from 30% to 70 % in steps of 10 % for speeds 1 –5.
The user sets the speed using a series of 5 switches . One for each speed.

## Slide 3: Q1
The user then closes the ON switch to turn on the motor.
When the users presses OFF switch the motor has to be closed(only one switch can be closed at any time).
Seven segment displays are available on which the duty cycle of the PWM signal is displayed.
The displays are always enabled and display the value ‘00’ when the motor is not rotating.
The only clock signals available in the system are the 5MHz system clock and 2.5MHz PCLK.

## Slide 4: Q1 contd..
The following interfacing devices are available:
  8255 - 01 no.
  Mapped to address 80H, 82H, 84H, 86H.
  8253 - 01 no.
  Mapped to address 88H, 8AH, 8CH, 8EH.
  A BCD to seven segment decoder- 02 nos.
  Any number of OR gates and inverters for address decoding.

## Slide 5: Q2
Design a system that generates an interrupt and turns on an LED connected to PC0 if the frequency drops below 1KHz.
The interrupt input of this is connected to IR0 of slave 8259. the slave 8259’s INT is connected to IR4 of master.
Base Address
  8254 10H
  8259M 18H
  8259S 20H