## Slide 1: Tutorial - 6
Module 4

## Slide 2: Question 1
n 32-bit data are stored starting from memory location dat1.
Write an ALP that will insert the string “????” after every mth double word
The value of m can range between 2 to 4 and is stored in location off1.
The value of n is between 10d to 120d and is stored in location cnt1.
The size n need not be a multiple of m

## Slide 3: Algo 1
Store data from dat1 into temp location
Find the new count based on increase in data size
Load offset no. of data from temp loc back into dat1
Update Count – If count = 0 stop
Load data ‘????’into dat1
Update Count – if Count = 0 go to step 3
cnt1 + (cnt1/off1)

## Slide 4: Question 2
n 16-bit data are stored starting from memory location dat1.
Write an ALP that will delete every mth word
The value of m can range between 2 to 8 and is stored in location off1.
The value of n is between 10d to 120d and is stored in location cnt1.
The size n need not be a multiple of m

## Slide 5: Question 3
Write an ALP that will scan a database of grades – the grades are to be stored as follows in memory: The id followed by grade.
Fine grading is used so if grade is A it stored as “A ” (A followed by space) and if the grade is A – it is stored “A-”.
For e.g. for 2 students the storage in memory will be as follows:
‘2014A3PS238G’, ‘A ’, ‘2014A7PS211G’, ‘B-’,
The count of students is available in location cnt1 (10d -100d).
The database of student ids and grades are available from location dat1.
Your ALP must find the id of students who have scored a particular grade and store the ids alone starting from location res1.
The grade that is been scanned for I stored in location grd1
The ALP must also find out how many students have scored the required grade and store it in location acnt1.

## Slide 6: Question 4
Write an ALP to multiply 2 64-bit unsigned number to get a 128-bit result
The two numbers are stored in location dat1 and dat2
The result is to be stored in location res1

## Slide 7: Question 5
Write an ALP to multiply 2 64-bit signed number to get a 128-bit result
The two numbers are stored in location dat1 and dat2
The result is to be stored in location res1