## Slide 1: Tutorial 9
Module 8 – 8.1,8.2,8.3

## Slide 2: Question 1
Distinguish between vectored and non-vectored interrupts with an example
Build a hardware circuit that can take in 8 interrupt requests as inputs and generate vector nos. (40H – 47H ) for these interrupt requests
  What are the main issues with this circuit ?

## Slide 3: Question 2
There are set of 8 LEDs connected to Port C of 8255- a logic low turns on the LEDs.
Write a code snippet that will turn on the LEDs connected to the even bits of Port C using BSR mode.
8255 is mapped to address 00H
Show the complete hardware interfacing circuit from the system bus onwards.

## Slide 4: Question 3
12 switches (1 to 12) are connected to 8086 through 8255. The 8086 system has identify the number of the switch closed and display it on two 7-segment displays available.
The 7-segment displays are of type common anode and can be interfaced using 7447.
The starting address of 8255 is 00H
Show the complete h/w interfacing circuit and the ALP to read switch closed and display the same on 7-segment displays
You can assume that only one switch will be closed at a time