## Slide 1
Microprocessor, Programming & Interfacing
Tutorial 2- Module 3

## Slide 2: Question 1
The instruction MOV DS, 2300h gives an error.
Why?

## Slide 3: Question 2
For the following instructions determine the addressing mode and the Machine code.
Assume instructions are in 16-bit mode of operation
(Contd.)

## Slide 4
MOV ECX ,CC001267H
MOV AX,SI
MOV [SI],CL
MOV AX,CS:[DI+1000h]
MOV CL,[EDX+EDI]
MOV EAX,4020[BX+DI]
MOV BX,[EBX+2*ECX]
MOV BL,SS:[ECX]
MOV CX,CX

## Slide 5
Question 3
(Contd.)
CS =1000H
ES = 8000H
DS =A000H
SS =7000H
ESI = 0000 0200H
EDI = 0000 0410H
EBP = 0000 2300H
EBX = 0000 0200H
EAX =0000 0400H
ECX = 0000 0020H
EDX = 0000 0008H

## Slide 6: For the instructions given below determine the machine code, address & addressing mode. Processor is working 32-bit mode
MOV [SI+100 H ],EAX
MOV [EAX+2*EBX],CL
MOV DX,CS:[EBX+4*EAX+1000 H]
MOV [BP+SI+2000 H],CX

## Slide 7: Question 4
Determine the instruction from the opcode assume the processor is working in 16-bit mode. All instructions are some form of MOV.
  66 89 D8
  89 46 10
  B1 45
  67 8A 44 7D 02

## Slide 8: Question 5-In an 80386 processor that is working in real mode and 16-bit mode
CS =0000H
ES = F000H
DS=4000H
SS = 2000H
ESI = 0000 0100H
EDI = 0000 0210H
EBP =0000 0300H
EBX=0000 4000H
EAX=0000 0200H
ECX= 0000 0010H
EDX= 0000 0004H
(Contd.)

## Slide 9: For the instructions given below determine the following: Memory Address, Addressing Mode and Machine Code. [Give Values only in Hex and treat instructions as separate individual instructions.]
MOV ES: [1000H], AH
MOV EAX, SS:[EBX+ 8]
MOV CH,[SI+BP+100H]
MOV EAX, [SI+BX]
MOV AL, [EBX+8*ECX+20H]