## Slide 1: Microprocessor Programming & Interfacing
Tutorial 1
Module 1 &2

## Slide 2: Question 1
What will be the result and what will be the nature of the result in terms (All operations should be done using sign- magnitude form of representation)
  is the result zero?
  is there a carry
  is there an auxiliary carry?
  is the result negative?
  is there an two’s complement overflow?
  is the result even or odd parity

## Slide 3: Question 1
(a) 44 + 52
(b) 97 + 48
(c) 99 - 33
(d) 33 - 99
(e) -29 + -32
(f) -41 - 95
(g) 100 + 28
(h) 27 – 100
AC | P | C | O | S | Z
AC | P | C | O | S | Z
1 | E | 0 | 0 | PL | 0
AC | P | C | O | S | Z
1 | E | 0 | 0 | PL | 0
0 | O | 0 | 1 | NG | 0
AC | P | C | O | S | Z
1 | E | 0 | 0 | PL | 0
0 | O | 0 | 1 | NG | 0
0 | E | 0 | 0 | PL | 0
AC | P | C | O | S | Z
1 | E | 0 | 0 | PL | 0
0 | O | 0 | 1 | NG | 0
0 | E | 0 | 0 | PL | 0
1 | E | 1 | 0 | NG | 0
AC | P | C | O | S | Z
1 | E | 0 | 0 | PL | 0
0 | O | 0 | 1 | NG | 0
0 | E | 0 | 0 | PL | 0
1 | E | 1 | 0 | NG | 0
0 | E | 1 | 0 | NG | 0
0 | E | 1 | 1 | PL | 0
AC | P | C | O | S | Z
1 | E | 0 | 0 | PL | 0
0 | O | 0 | 1 | NG | 0
0 | E | 0 | 0 | PL | 0
1 | E | 1 | 0 | NG | 0
0 | E | 1 | 0 | NG | 0
AC | P | C | O | S | Z
1 | E | 0 | 0 | PL | 0
0 | O | 0 | 1 | NG | 0
0 | E | 0 | 0 | PL | 0
1 | E | 1 | 0 | NG | 0
0 | E | 1 | 0 | NG | 0
0 | E | 1 | 1 | PL | 0
1 | O | 0 | 1 | NG | 0

## Slide 4: Question 2
Three, 16 bit numbers are stored in memory location ‘a’,’ b’ and ’c’.
Write ALP programs for adding the 3 numbers for CISC and a RISC processor.
Assume that CISC processor has two temporary storage registers and RISC processor has 8 registers.
The result is to be stored in memory location ‘d’. The instructions involving ALU follow 3 operand format.
Compare the performance of the CISC & RISC Processor.

## Slide 5: Question 2
CISC
add r1,a,b
add d,r1,c
RISC
ld r1,a
ld r2,b
ld r3,c
add r1,r1,r2
add r1,r1,r3
st d,r1

## Slide 6: Question 3
Given the following ALU chip (ALU 181)
S3 – S0 -Selects ALU operation to perform
M (1–Logical, 0-Arthimetic )
CIN
C4 along with A= B can be used for unsigned comparison
A0-A3
B0-B3
F0-F3
C’in
M
C4
A=B
S0-S3

## Slide 7: Question 3
What will be the size of CPU built around this ALU
(b) If other than ALU operations- the processor performs
  Load data from mem to reg
  Store dats from reg to mem
  Move data from reg to reg
  1 Unconditional Branch
  4 Conditional branches
  1 Call
  1 Return
And Instruction is of the format – Opcode dst,src , All ALU operations are performed on registers, There are totally 16 Registers R0- R15 .
What will be the normal size of the instruction?

## Slide 8: Question 3
(c) What type of Architecture does the processor implement?
(d) 64K and Memory is byte organized- How many address are required?
(e) What will the number by which the Program Counter be incremented to support the normal sized instruction?
(f) Can you think of any other major digital modules that the processor may require?

## Slide 9: Question 4
If CS=2000 and IP= FFFE. What is the next address generated for fetching the instruction by 8086 processor

## Slide 10: Question 5
Why is instruction pointer generally incremented by 2 in 8086 processors?

## Slide 11: Question 6
If the starting address of various segments of 8086 processor is given as follows, find the ending address.
Segment | Starting Address | Ending Address
Code Segment | F0000 | 
Data Segment | 30000 | 
Extra Segment | 00000 | 
Stack Segment | AB000 | 
Segment | Starting Address | Ending Address
Code Segment | F0000 | FFFFF
Data Segment | 30000 | 
Extra Segment | 00000 | 
Stack Segment | AB000 | 
Segment | Starting Address | Ending Address
Code Segment | F0000 | FFFFF
Data Segment | 30000 | 3FFFF
Extra Segment | 00000 | 
Stack Segment | AB000 | 
Segment | Starting Address | Ending Address
Code Segment | F0000 | FFFFF
Data Segment | 30000 | 3FFFF
Extra Segment | 00000 | 0FFFF
Stack Segment | AB000 | 
Segment | Starting Address | Ending Address
Code Segment | F0000 | FFFFF
Data Segment | 30000 | 3FFFF
Extra Segment | 00000 | 0FFFF
Stack Segment | AB000 | BAFFF

## Slide 12: Question 7
CS:2100 IP: FFFC
CS:FE00 IP:ABBE
CS:3220 IP:2140
CS:F000 IP:A1C4
30FFC
08BBE
34340
FA1C4
For the Following Combinations of CS& IP what will be the physical address

## Slide 13: Question 8
CS:2000 EIP: 000010AC
DS:C000 ESI: 0000AB00
SS:8000 ESP:00000900
210AC
80900
CAB00
Determine the memory locations addresses by the following registers in real mode

## Slide 14: Question 9
Based on the contents of Flag Register of 8086 after the add operation – what can you say about the type of result?
0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
 |  |  |  | O | D | I | T | S | Z |  | A |  | P |  | C