## Slide 1: Microprocessor, Programming & Interfacing
Tutorial 4 – Module 4

## Slide 2: Question 1
Register Content
AX = 1111
CX = 2222
DX = 3333
BX = 4444
BP = 5555
SI = 6666
DI = 7777
SP = 3000
(All values are in hex)
Program
PUSHA
PUSH AX
POPA
POP AX

## Slide 3: Question 2
SP=3000H
SI=0250H
BX=2345H
AX=6789H
DI= 0100H
Flag register is 0231H
PUSH AX
PUSH BX
PUSHF
PUSH 0987H
PUSH DI
PUSH SI
POP AX
POP BX
POPF
POP DI
POP [SI]

## Slide 4: Question 3
Write an 80486 ALP with a subroutine ‘sub1’ that will count number of odd positive, odd negative, even positive and even negative 32-bit numbers.
The data that is to be analysed is stored in memory location ‘in1’ and results will be stored in locations ‘oddpos’, ‘oddneg’, ‘evenpos’,’evenneg’ respectively.
The total count of data available is in location ‘cnt1’ and cannot exceed 100.
The subroutine should do the categorization and counting while the main program only passes the number as a parameter using SI as the pointer

## Slide 5: Question 4
Write an 80486 ALP that will examine a series of memory locations for small alphabets.
If a memory location has a small alphabet it will convert it into capitals.
If the memory location does not have a small alphabet it will not modify the contents of the memory location.
The series of memory location to be examined start at alph1. The count of memory locations to be examined is stored in cnt1 and will not exceed 1000d.
The checking and the conversion of one small alphabet to one capital alphabet must be done using a macro called CAPSON.

## Slide 6: Question 5
Write an ALP that will find out whether data stored in loc1 is a palindrome.
The size of the palindrome is stored in location cloc1.
Make this as a sub program –that can be accessed by a main program that handles array of numbers.
The count of the palindrome must be stored in location dloc1.